STICKY MAT (I-5240)      		User's Manual

General information

The STICKY MAT with dimensions of 15 x 15 cm, makes the use of fixing clips unnecessary in many situations. It is designed for holding glassware (e.g. Erlenmeyer flasks) in place on all types of shaking tables used with shakers and shaking incubators. The glassware used must have a flat, even base.

Safety instructions

• Always wear personal protective equipment in accordance with the hazard class of the media being worked with.

• The surface of the STICKY MAT and vessels must be free of grease, oil, dirt and moisture.

• Do not exceed the maximum load indicated for the device.

• Check all vessels placed on the STICKY MAT for damage. Never use damaged vessels.

• Ensure that no condensation forms on glassware when used in a shaking incubator.

Fitting

The STICKY MAT is suitable for use with all types and sizes of shaking tables. Where necessary, the STICKY MAT can be cut to the desired size.

• Degrease the shaking table if necessary (e.g. with isopropanol).

• You can moisten the shaking table with water to allow easy positioning of the STICKY MAT.

• Remove the protective film from the bottom side of the STICKY MAT - flat side without lowered edge.

• Place the STICKY MAT on the shaking table with the bottom side down.

• If you moistened the shaking table, the film of water allows the STICKY MAT to be moved around for precise positioning. Remove excess water and air bubbles using a ruler or similar straight edge device and mop it up

with a cloth.

• The STICKY MAT must be completely dry before the first use, so allow it enough time to dry up. Finally, remove the second protective film on the upper side of the STICKY MAT.

Use, cleaning and maintenance

Ambient temperature                           5 to 80°C Maximum shaker speed                      300 RPM Maximum load                                     3 kg

Avoid direct sunlight and strong UV light.

• To remove the vessel, push or pull it gently to the side at the top and wait for a few seconds, until the vessel slowly releases.

• The STICKY MAT can be removed from the shaking table by pulling it to the side diagonally.

• Clean the STICKY MAT with a damp, lint-free cloth and a mild detergent.

• Disinfect it using e.g. 70 percent ethanol.

• The sticky properties of the material can be refreshed by moistening the STICKY MAT with water.